## Slide 1: Intro to Radiology
Presented by: Aaron Perry, PA-C
INTRO TO RADIOLOGY
Part I

## Slide 2: RADIOLOGY
Imaging is a powerful tool in the pursuit of a diagnosis
Imaging is used to identify:
  The patient’s anatomy and any alterations to the normal anatomy.
  The patient’s physiology either directly with dynamic real-time images or indirectly by seeing alterations to normal tissue.
Imaging modalities differ in how they “see” the body, primarily using the water in our bodies to detect and process images.

## Slide 3: RADIOLOGY
The goal is to select the best modality to investigate the possible diagnoses.
This depends on:
Which area of the body is being studied
What your diagnostic suspicion is, your differential diagnosis.

## Slide 4: RADIOLOGY
All imaging studies have associated cost and possible associated risk. Understanding these factors help us make wise decisions.

## Slide 5: WORKING IN RADIOLOGY
The clinician working in radiology must combine knowledge of imaging physics and anatomy with a broad fund of medical knowledge to arrive at a diagnosis relevant to the patient's clinical presentation.
Effective communication between the referring clinician and the radiology clinician is vital in all stages of imaging

## Slide 6: WORKING IN RADIOLOGY
Examples of commonly performed procedures by PAs include:
  Chest tube placement and PleurX catheter placement
  Diagnostic paracentesis and thoracentesis
  Diagnostic lumbar punctures
Physician assistants working in radiology often work on the intervention side of the specialty

## Slide 7: RADIOLOGY TERMS
Planar images are shadows of complex three-dimensional objects. These images compress a large amount of information into a two-dimensional image; however, when compressed, important data may be obscured.
A CXR is an example of a planar study

## Slide 8: RADIOLOGY TERMS
Depending on the modality, images can be acquired in two or three dimensions. The images can be mathematically manipulated to obtain two-dimensional images in different planes or three-dimensional images highlighting specific regions or anatomy.
Cross-sectional imaging techniques depict the three-dimensional reality of human anatomy by creating a detailed composite analysis in two-dimensional “slices”.
  CT, ultrasound and MRI are cross-sectional imaging modalities

## Slide 9: RADIOLOGY TERMS
Artifact: an imaging finding that does not directly correspond to the reality of the patient and may mimic a clinical feature, degrade image quality, or obscure anatomy.
Image contrast is the difference in brightness between an area of interest and its surroundings. The larger the difference in brightness, the easier it is to differentiate one structure from another.
When looking at a CT, the perspective is from the patient’s feet.

## Slide 10: RADIOLOGY TERMS
Attenuation: refers to the reduction in the intensity of an x-ray beam as it passes through matter due to either the absorption or scattering of photons.
Different materials in the body will attenuate x-rays to different degrees to help produce images.
  X-rays pass through air-filled lungs with little attenuation, but the x-ray beam is substantially attenuated when passing through bone.

## Slide 11: CONTRAST AGENTS
Contrast agents, such as iodine and barium, are most commonly positively enhancing an image and result in attenuation of the x-ray beam which increases image contrast.
Contrast agents can be administered through any cavity (natural or iatrogenic) and enhance a difference between tissues that would normally have similar x-ray absorption.

## Slide 12
Barium sulfate: cheap, used in fluoroscopic and CT studies to opacify the GI tract. Generally, well tolerated, but can cause peritonitis if spilled into the abdominal cavity in cases of perforation.
Barium Swallow:
CONTRAST AGENTS
https://youtu.be/fqG0QmlaFMs?si=dDDP-19_k95-Q_1C

## Slide 13
2nd and 3rd generation iodinated contrast agents are given IV to create contrast during CT image acquisition. Often, contrast agent administration is timed to increase detection of pathology.
CONTRAST AGENTS
Non-Contrast CT
CT w Contrast

## Slide 14
Non-Contrast CT
Contrast CT

## Slide 15
Precisely timed iodinated IV contrast agents move quickly into the extracellular fluid and are excreted primarily by the kidneys.
Dynamic contrast-enhanced imaging refers to precise timing of the contrast injection and image acquisition. This technique can help identify and classify abnormalities by taking advantage of the difference in contrast enhancement among different tissues across time.
        For example, a lesion can have the same attenuation as its surroundings on non-contrast and delayed contrasted images, but will have intense enhancement on arterial phase images (When contrast is first administered)
CONTRAST ROUTES: INTRAVENOUS (IV)

## Slide 16
  Angiogram: Visualization of specific arteries either by direct injection of Iodine contrast into a specific artery or by IV injection. Visualization with either fluoroscopic images or computed tomography angiogram (CTA)
CONTRAST ROUTES: ARTERIAL

## Slide 17
By mouth (PO) or per rectum
  Oral contrast enhances the GI tract from mouth to rectum
  Double contrast is often used in the rectum- distending the colon with air and then barium
  Intravenous (IV)
    Enhances any inflammation, better defines the organs and tumors
CONTRAST ROUTES: GI

## Slide 18: CONTRAST ROUTES: GU
Hysterosalpingogram: catheter is used to administer Iodine contrast into the cervical canal to visualize the uterine cavity and fallopian tubes
Cystogram: a foley catheter is used to administer Iodine contrast into the bladder retrograde. Can also visualize the bladder filled with contrast after it has traveled through the venous system and enters the urinary system

## Slide 19
Intrathecal
  Myelogram: Iodine contrast injected into the subarachnoid space in the nervous system for imaging of the spine and nerve roots.
Kidneys
  Nephrostogram: Direct injection of Iodine contrast into the kidney via a nephrostomy tube with fluoroscopic visualization of kidneys, ureters and bladder antegrade.
  Intravenous pyelogram (IVP): contrast injected in the venous system with delayed radiographic images lighting up the renal pelvis.
CONTRAST ROUTES

## Slide 20
Renal impairment
  Important with IV iodine or gadolinium contrast as these are cleared by the kidneys. Evaluate the eGFR before ordering to determine benefit versus risk.
Pregnancy
  Generally, CT is avoided in pregnancy but can be used after risk-benefit assessment. Low osmolality iodinated contrast is considered appropriate when diagnostically needed.
CONTRAST CONSIDERATIONS

## Slide 21
GI perforation
    Water-soluble contrast agent, such as Gastrografin, should be used when the clinician is looking for esophageal or bowel perforation, obstruction, or when a surgery is planned as Barium causes severe peritonitis
Allergies and medications
  Modern iodinated allergic-like reactions are uncommon (about 0.6% overall, 0.04% severe). Reactions range from mild such as hives and itching to severe, anaphylaxis.
  If a study must be done with contrast, an institutional premedication protocol may be used when indicated.
CONTRAST CONSIDERATIONS

## Slide 22
  Mild reactions occur when patients develop warmth, flushing, N/V, mild urticaria, scratchy throat. Treatment is observation ~ 30 minutes +/- benadryl
  Moderate reactions include severe urticaria, bronchospasm, transient hypotension and tachycardia. These require close monitoring until the symptoms resolve completely.
  Severe reactions include diffuse erythema, altered mental status, seizures, severe bronchospasm, laryngeal edema, severe hypotension, or sudden cardiac arrest.
IODATED CONTRAST REACTIONS

## Slide 23
Only about one third of patients with severe reactions have a prior history of reactions and pre-treatment to prevent these has very poor evidence showing efficacy for anything other than mild reactions.
Contrast extravasation is also potentially severe. Patients with extravasation will need close monitoring of skin and soft tissue. Typically, limb elevation and hot or cold compresses are used. Observation can range from several hours to overnight if needed. Watch for compartment syndrome and consider surgical consultation.
IODATED CONTRAST REACTIONS

## Slide 24
Contrast preferred:
Tumor
Intravascular pathology
  Clot, stenosis, ischemia of distal tissues, perforation, dissection
Inflammatory etiology
  colitis, encephalitis
Contrast is helpful:
Infection (most)
Contrast generally not needed:
Stroke
Bones or calcification
Lung parenchyma or pleura
General abdominal evaluation
When in doubt . . . Call radiology to ask!!
WHEN TO USE CONTRAST

## Slide 25: MODALITIES USING IONIZED RADIATION
Radiography: commonly called x-rays, they are the oldest imaging modality
Fluoroscopy are sequential x rays seen real-time to produce a dynamic moving study. It is useful for evaluating function.
      Barium Swallow video https://www.youtube.com/watch?v=1-I3lDjGvcs
Computed Tomography (CT) scan uses a moving x-ray tube and moving detector to capture and process cross sectional images in different body planes

## Slide 26
Mammography uses low dose radiation to image the breast. Routine diagnostic mammograms are essential in the early detection of breast malignancies.
MODALITIES USING IONIZED RADIATION
Densitometry - Dual Energy X-ray Absorbitometry (DEXA) uses low dose radiation to evaluate bone mineral density. It is used to screen for osteoporosis and guide therapeutic intervention.

## Slide 27
Ionizing radiation means enough energy is produced to displace orbiting electrons, forming ions aka free radicals.
These unstable molecules can bind to organic material causing a change in cellular metabolism. Free radicals can also bind to DNA causing mutation or cell death.
EFFECTS OF IONIZING RADIATION

## Slide 28
Female of reproductive age (6-60 y/o)
Gonadal cells are more sensitive to ionizing radiation at high dose, much higher than most diagnostic imaging studies. Caution is advised.
Carcinogenesis from in utero radiation can lead to childhood malignancy.
Children
Their young rapidly dividing cells are more prone to the harmful effects of ionizing radiation, i.e. mutations.
Can impact all cell lines leading to risk of malignancy
EFFECTS OF IONIZING RADIATION: CONSIDERATIONS

## Slide 30: SPECIAL NOTE ON DIAGNOSTIC MAMMOGRAPHY
For most women, the benefits of regular mammograms outweigh the risks posed by the small amount of radiation.
The risk associated with this dose appears to be greater among younger women (under age 40).

## Slide 31: XRAY

## Slide 32: RADIOGRAPHY
Radiography, the use of x-rays to generate images, is the oldest of the imaging modalities used in diagnostic radiology.
The words x-ray, plain film, radiograph, and conventional radiograph are used interchangeably to refer to radiography.
Fluoroscopy is an application of radiography that allows real-time observation of internal structures of a patient and is used predominantly in gastrointestinal imaging, interventional radiology, and musculoskeletal radiology.

## Slide 33: SCIENCE OF RADIOGRAPHY
X-rays are part of the electromagnetic spectrum, like visible light and radio waves, but are at a much higher frequency.

## Slide 34: SCIENCE OF RADIOGRAPHY
The different densities of our body’s tissues will either absorb, reflect (scatter), or allow the x rays to pass through without change.
A digital detector (or film) on the other side of the patient, will quantify the number of x-rays that have passed through the differing body densities and produce the image that we see in a 2D grayscale image called radiographs.

## Slide 35: THE RADIOGRAPH
Air appears BLACK
Fat appears DARK GREY
Water appears LIGHT GREY
Bone appears WHITE
Metal/contrast appears BRIGHT WHITE
The number of x-rays that pass through depends on the density of the tissue (relative to water)
  The more x rays that pass through, the darker the image
  If fewer x rays that pass through, the lighter the image

## Slide 36: TISSUE DENSITY & XRAY APPEARANCE
Tissue Type | Density Relative to Water | X-ray Attenuation | Appearance on X-ray/CT | Examples
Air | Least dense | Minimal attenuation | Black | Lungs, bowel gas
Fat | Less dense than water | Low attenuation | Dark gray | Subcutaneous tissue, mesentery
Water / Soft Tissue | Reference point (CT = 0 HU) | Moderate attenuation | Light Gray | Muscles, organs, blood
Bone | Very dense | High attenuation | White | Ribs, skull, spine
Metal / Contrast | Extremely dense | Max attenuation | Bright white | Prosthetics, calcifications, iodinated contrast

## Slide 37: XRAY Penetration
Under-penetrated CXR
Over-penetrated CXR
The penetration of the film refers to how well the X-rays have passed through the patient and been detected by the image detector.

## Slide 38: PROJECTIONS
The “projection” refers to the path the beam takes through the body
Because radiographs are flat 2D images, multiple projections are taken to see several angles of the area of interest.
You will see orders written 2 view, 3 view, etc. This refers to different projections: anteroposterior (AP), posteroanterior (PA), lateral or oblique.

## Slide 39: PROJECTIONS
PA Projection
AP Projection
*Note the difference in image quality between the two as well.
PA
AP

## Slide 40: XRAY APPLICATIONS
Evaluation of bones or pathology of bones (lesions/malignancy)

## Slide 41: XRAY APPLICATIONS
Good for imaging gas or air that define body structures when the ACUITY IS LOW.
  Lungs
  Gastrointestinal tract
Can visualize some organs and soft tissues and calcifications within them, for example, kidney stones
Can also find foreign bodies that are dense, i.e. metallic objects

## Slide 42: WHEN DO WE USE GENERAL RADIOGRAPHY OVER OTHER MODALITIES?
Initial diagnosis of bony structures in the outpatient and emergent settings
  fractures, bone lesions/tumors or degenerative changes (ie. arthritis)
A “first look” at many pathologies when the ACUITY IS LOW.
  Uses less radiation than CT
  Less costly, insurance companies often require a general radiograph in outpatients before ordering more extensive (expensive) imaging modalities
Ease of use and portability: can be done at bedside with the patient in any condition!

## Slide 43: COMPUTED TOMOGRAPHY (CT)

## Slide 44: THE SCIENCE OF COMPUTED TOMOGRAPHY (CT)
The donut-shaped gantry contains the radiation source (x-ray tube) and detectors of the CT scanner.
The examination table carries the patient through the gantry while images are obtained by rapid rotations of the x-ray tube around the patient.

## Slide 45: THE SCIENCE OF COMPUTED TOMOGRAPHY (CT)
Essentially, a narrow beam of x-rays passes through a section of the patient and sensitive detectors on the other side measure the transmitted x-rays.
Computer processing of the data constructs a cross-sectional image of the body in slices.
More intense computational processing can also produce 3D images.

## Slide 46: THE SCIENCE OF COMPUTED TOMOGRAPHY (CT)
Unlike radiographs, the differences in density on CT is quantifiable and is assigned a value on the Hounsfield unit (HU) scale. The numbers are, by convention, compared to the average attenuation value of water.
Water is assigned a value of 0 HU. The scale ranges from approximately –1000 HU (black) for air to greater than +1000 HU (white) for metal.

## Slide 47: READING A CT SCAN
The data can be reconstructed to view in different body planes: axial, coronal and sagittal

## Slide 48: AXIAL PLANE
An axial CT image is displayed as if the clinician is standing at the patient's feet looking up
The axial plane is most commonly used, and the clinician scrolls through a series of images- going up and down the area imaged.

## Slide 49: SAGITTAL PLANE
A sagittal CT image is displayed as if the clinician is standing at the patient’s left shoulder and viewing slices of the body area as they pass to the right shoulder.

## Slide 50: CORONAL PLANE
A coronal CT image is displayed as if the clinician is standing in front of the patient and viewing slices of the body area under evaluation from the front to the back.

## Slide 51: READING A CT SCAN
The human eye cannot effectively differentiate between all the shades of gray that make up the full spectrum of attenuation values in a CT image (-1000 to 1000 HU).
To make a CT easier to read, the clinician establishes a limited view of the CT by selecting those Hounsfield units that will best look at what they want to see.
A radiologist performing an official reading of a CT will do this multiple times to look at tissues of varying densities.

## Slide 52: READING A CT SCAN
Here is how it works:
A limited gray scale is established by reducing the number of Hounsfield units being displayed by setting a “window width” – for example: -100 HU to 500 HU.
This also sets a “window level” in the exact middle of the scale, in this example the level would be 200 HU
The window width sets parameters so that only HU in that range are included. Those above and below the window width limits are displayed as white and black, respectively.

## Slide 53
Window width: the window width refers to the number of different HU units that will be represented by different shades of gray. Any HU value that falls below the lower value of the window width will show up as BLACK on the scan while any HU value that is above the upper value of the window width will be WHITE.

## Slide 54: READING A CT SCAN
Increasing the window width will DECREASE the contrast of the image because a larger change in density will be required to change the shade of grey represented by a HU. Decreasing the window width will INCREASE the contrast of the image.
Note the ability to detect the muscles and fat in the subcutaneous tissues of the chest wall is significantly reduced when the window width is increased from 400 to 1,000.

## Slide 55: READING A CT SCAN
So, when a clinician reads a CT scan, they will look at the images multiple times. Each time they will look at different structures using a window width and level that brings those areas into sharper focus.
For example, when a radiology clinician reads a chest CT, they will look at
  At bone windows to evaluate the ribs, sternum and spine
  At lung windows to evaluate the lung parenchyma
  At chest windows to evaluate the vascular structures and the air- filled bronchi/ trachea

## Slide 56: 3 DIMENSIONAL CT RECONSTRUCTIONS
Surface rendering of the spine
Volumetric rendering of the thoracic spine with hardware (red)
CT reconstruction of the distal aorta

## Slide 57: CT APPLICATIONS
CT is a common imaging choice when evaluating the viscera because they can be viewed from many cross-sectional planes and the organs readily enhance with contrast, providing optimal definition.
CT provides an excellent look at the:
  Small/large bowel
  Liver
  Pancreas
  Spleen
  Lungs
  Brain

## Slide 58
CT is an excellent modality for imaging vascular structures and evaluate for any evidence of active bleeding- contrast extravasation. Evaluation of the vasculature does require the use of IV contrast.
A= the abdominal aorta
B= contrast extravasation
C= a large fluid collection with gas
CT APPLICATIONS

## Slide 59
CT is used for imaging the fine detail of bony structures. However, more radiation is used, and the CT is more costly, so plain radiographs are typically used first line to evaluate the bones.
If radiographs are not diagnostic of a fracture, further evaluation with CT is warranted if the clinician suspects an occult fracture.
CT is generally chosen to evaluate bony structure of skull and spine after traumatic injury due to the level of detail often needed in these areas.
CT APPLICATIONS

## Slide 60
Am I able to image my pregnant patient with another modality?
    Risk/benefit assessment should be done in this population to avoid undue radiation to the fetus
CT uses much more radiation than a plain radiograph.
  Has the patient received multiple CTs and or received a large radiation dose over time?
  Can another test be ordered to make my diagnosis?
CT CONSIDERATIONS

## Slide 61
Is my patient able to hold still for the test?
  A moving patient causes imaging artifact, creating a blurry and nondiagnostic study. Repeat of the test to obtain an optimal image exposes the patient to additional radiation.
  An important consideration in small children, encephalopathic patients and those with dementia who may not be able to remain still.
  Less of a concern for CT- which acquires images quickly and much more of an issue for MRI which has a longer image acquisition time and a more claustrophobic environment.
CT CONSIDERATIONS

## Slide 62: WITH OR WITHOUT CONTRAST?
Obtain a CT WITHOUT contrast if:
The patient has a contraindication to the administration of iodinated contrast- prior severe allergic-like reaction to iodinated contrast. Reduced eGFR or AKI must also be taken into account
Contrast does not enhance the area of interest thus it is not needed for diagnosis.
  If the examiner is looking at bone, calcifications, kidney stones
  Lung pleura and parenchyma- except in cases of malignancy. Lung infection can be seen without contrast.

## Slide 63: WITH OR WITHOUT CONTRAST?
Obtain a CT WITH contrast for:
Enhancement of inflammatory processes
  “Fat stranding” seen in inflammatory processes such as diverticulitis or appendicitis.
  Evaluation of infectious process/abscess
Evaluation of vascular structures, ie. aorta and arterial branches, order a CT angiogram or CTA- not a CT with IV contrast.

## Slide 64: WITH OR WITHOUT CONTRAST?
Obtain a CT WITH contrast for:
Suspected malignancy
  Contrast will help to differentiate normal from abnormal tissue and to identify metastasis.
  Hypervascular lesions will readily enhance with IV contrast
  Some lesions are hypovascular compared to surrounding structures.
Different phases of enhancement based on blood flow are found in the liver, pancreas and kidney. The radiologist may suggest a particular “protocol” for imaging these organs in order to take advantage of this to make a diagnosis.

## Slide 65
A CT with IV contrast is timed to begin the scan at the optimal time to enhance organs, soft tissues, and vessels (arterial vs. venous)
A CT angiogram (CTA) specifically looks at the vasculature of the body using contrast.
CT WITH CONTRAST VS
CT ANGIOGRAM (CTA)